## Slide 1
Project Apollo
An open source oxygen concentrator

## Slide 2
Why
  Ventilators need oxygen!
    Typical FiO2 0.3 … 1
  Oxygen generation is a big problem in developing countries.
    No established infrastructure.
    Oxygen bottles are expensive
  People are already looking at alternative (local) ways for producing oxygen
Project Apollo

## Slide 3
What is it
  Goal = enabling people around the world to build the prototype ASAP
  Focus = Simplicity and speed of build
    Simple, reliable design (zeolite-based PSA system)
    Flexible, open source, off-the-shelf materials
    Very low cost (aspirational target = $200 for 15 liters/min @ 80%)
  Final goal = Enable people to iterate and publish their own designs in the community
Project Apollo

## Slide 4
How to build it
  Follow the published build documentation
  Buy/source the materials (check out the BOM)
  Build the prototype
  Validate O2 concentration and flow. Use a good reference O2 and flow sensor for calibration
Multiple iterations/variants have been built
  O2 concentration 45 … 70%, 5 lpm
Project Apollo v2

## Slide 5
Project Apollo v4
Apollo Control Box v4
  Focus = medical device
    Safety: detect all failure scenarios
    Ease of use: User experience and maintainability. Clear, actionable error messages
    Self-regulating: Patient sensor/data feedback loop
  Prototype: Self-contained control box
    Touch screen for diagnostic messages, medical-grade buzzer
    Open source, modular PCB design. Works with a variety of sensors
    Self-tuning: valve timing, auto-adjusts to changes in compressed air input pressure, machine learning
    Integration with SpO2 oximeter Bluetooth sensor
    Cloud data integration for patient monitoring
Collaborations
  Helpful Engineering, Public Invention, Oxikit, Microsoft Garage, Quick2space.org
Documentation, code
  http://project-apollo.org

## Slide 6
Thank you!