## Slide 1
Project Apollo
An open source oxygen concentrator
http://project-apollo.org
#project-oxygen-concentrator

## Slide 2
Why
  O2 needed for ventilators, oxygen therapy
    Typical FiO2 0.3 … 0.5, up to 1
  Oxygen generation is a big problem in developing countries
    No established infrastructure
    Oxygen bottles are expensive
  People are already looking at alternative (local) ways for producing and delivering oxygen
Project Apollo
https://www.economist.com/graphic-detail/2021/03/09/hospitals-are-running-out-of-oxygen-to-treat-covid-19-patients
https://www.cidrap.umn.edu/news-perspective/2021/03/who-sounds-alarm-over-covid-linked-oxygen-crisis
https://apnews.com/article/oxygen-crisis-africa-latin-america-eb0d2731a8613c1ae218db7d32a227a6

## Slide 3
What is it
  Goal = enabling people around the world to build the prototype ASAP
  Focus = Simplicity and speed of build
    Simple, reliable design (zeolite-based PSA system)
    Flexible, open source, off-the-shelf materials
    Very low cost (aspirational target = $200 for 15 liters/min @ 80%)
  Final goal = Enable people to iterate and publish their own designs in the community
Project Apollo

## Slide 4
How to build it
  Follow the published build documentation
  Buy/source the materials (check out the BOM)
  Build the prototype
  Validate O2 concentration and flow. Use a good reference O2 and flow sensor for calibration
Multiple iterations/variants have been built
  O2 concentration 45 … 70%, 5 lpm
Project Apollo v2

## Slide 5
Project Apollo v4
Apollo v4
  Focus = medical device
    Safety: detect all failure scenarios
    Ease of use: User experience and maintainability. Clear, actionable error messages
    Self-regulating: Patient sensor/data feedback loop
  Control box
    Touch screen for diagnostic messages, medical-grade buzzer
    Open source, modular PCB design. Works with a variety of sensors
    Self-tuning: valve timing, auto-adjusts to changes in compressed air input pressure, machine learning
    Integration with SpO2 oximeter Bluetooth sensor
    Cloud data integration for patient monitoring
  Self-contained enclosure
    Built-in compressor
    Full focus on thermals, airflow, noise reduction
Collaborations
  Funding: Quick2space.org
  Volunteers: Helpful Engineering, Microsoft Garage, Public Invention
Documentation, code
  http://project-apollo.org

## Slide 6
Project Apollo v4
http://project-apollo.org

## Slide 7
Thank you!